## Slide 1
Nataliia Sheludiakova
January 2016
Test Design Techniques

## Slide 2
Agenda
Equivalence Partitioning
Boundary Values Analysis
Decision Tables
State Transition

## Slide 3: Equivalence Partitioning
Task: Internal telephone system for a company with 100 telephones has 3-digit extension numbers from 100 to 199. In a system designed to support registration of telephone number user should enter unique phone number and user’s first and last names.
Partitions should be designed for phone number field.
90
150
500
invalid | valid | invalid
- 99 | 100 199 | 200 +
invalid
000 099
050

## Slide 4: Boundary Values Analysis
Task: Internal telephone system for a company with 100 telephones has 3-digit extension numbers from 100 to 199. In a system designed to support registration of telephone number user should enter unique phone number and user’s first and last names.
Partitions should be designed for phone number field.
invalid | valid | invalid
- 99 | 100 199 | 200 +
99; 100
199; 200
98; 99; 100; 101
198; 199; 200; 201
Sometimes it’s better to use additional values to avoid defects - which are equal to ‘minus’ and ‘plus’ one number to boundary value.

## Slide 5: Decision Tables
Task: If you are a new customer opening a credit card account, you will get a 5% discount on all your purchases today. If you are an existing customer and works with bank more than a year, you will get a 15% discount. If you are a bank client and works with bank less than a year, you will get a 10% discount. If you have a coupon, you can get 20% off today (but it can't be used with the 'new customer' and ‘less than a year existing customer’ discounts).
Causes (inputs) | R 1 | R 2 | R 3 | R 4 | R 5 | R 6 | R 7 | R 8 | R 9 | R 10 | R 11 | R 12 | R 13 | R 14 | R 15 | R 16
New customer (5%) | Y | Y | Y | Y | Y | Y | Y | Y | N | N | N | N | N | N | N | N
Client <1 year (10%) | Y | Y | Y | Y | N | N | N | N | Y | Y | Y | Y | N | N | N | N
Client >1 year (15%) | Y | Y | N | N | Y | Y | N | N | Y | Y | N | N | Y | Y | N | N
Coupon (20%) | Y | N | Y | N | Y | N | Y | N | Y | N | Y | N | Y | N | Y | N
Effects (Outputs) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Discount (%) | x | x | x | x | x | x | 20 | 5 | x | x | 20 | 10 | 35 | 15 | 20 | 0
Error message | 1 | 1 | 2 | 2 | 3 | 3 | ? |  | 4 | 4 | ? |  | ? |  |  | 
new customer – 5% discount
bank client less than a year – 10% discount
bank client more than a year – 15% discount
coupon – 20% discount (can't be used with the 'new customer' and ‘less than a year existing customer’ discounts)
Error message 1 – ‘You cannot be both a new customer and also an existing customer for more and less than a year. Please try again.’
Error message 2 – ‘You cannot be both a new customer and also an existing customer for less than a year. Please try again.’
Error message 3 – ‘You cannot be both a new customer and also an existing customer for more than a year. Please try again.’
Error message 4 – ‘You cannot be both an existing customer for less and more than a year. Please try again.’
? - The 20% and 35% discounts are an assumption, and we should check that these assumptions are correct, by asking the person who wrote the specification.

## Slide 6: Decision Tables
Task: If you are a new customer opening a credit card account, you will get a 5% discount on all your purchases today. If you are an existing customer and works with bank more than a year, you will get a 15% discount. If you are a bank client and works with bank less than a year, you will get a 10% discount. If you have a coupon, you can get 20% off today (but it can't be used with the 'new customer' and ‘less than a year existing customer’ discounts).
Causes (inputs) | R 2 | R 4 | R 6 | R 7 | R 8 | R 10 | R 11 | R 12 | R 13 | R 14 | R 15 | R 16
New customer (5%) | Y | Y | Y | Y | Y | N | N | N | N | N | N | N
Client <1 year (10%) | Y | Y | N | N | N | Y | Y | Y | N | N | N | N
Client >1 year (15%) | Y | N | Y | N | N | Y | N | N | Y | Y | N | N
Coupon (20%) | N | N | N | Y | N | N | Y | N | Y | N | Y | N
Effects (Outputs) |  |  |  |  |  |  |  |  |  |  |  | 
Discount (%) | x | x | x | 20 | 5 | x | 20 | 10 | 35 | 15 | 20 | 0
Error message | 1 | 2 | 3 | ? |  | 4 | ? |  | ? |  |  | 
new customer – 5% discount
bank client less than a year – 10% discount
bank client more than a year – 15% discount
coupon – 20% discount (can't be used with the 'new customer' and ‘less than a year existing customer’ discounts)
Error message 1 – ‘You cannot be both a new customer and also an existing customer for more and less than a year. Please try again.’
Error message 2 – ‘You cannot be both a new customer and also an existing customer for less than a year. Please try again.’
Error message 3 – ‘You cannot be both a new customer and also an existing customer for more than a year. Please try again.’
Error message 4 – ‘You cannot be both an existing customer for less and more than a year. Please try again.’
? - The 20% and 35% discounts are an assumption, and we should check that these assumptions are correct, by asking the person who wrote the specification.

## Slide 7: State Transition
Task: User sends message using mobile phone. He enters a text of a message, and then phone number of recipient and click ‘Send’. Assume that delivery report option is enabled. If user gets positive delivery report, then message will be delivered to recipient. If not, then message will be stored on server for 12 hours. If recipient turns on the phone until 12 hours over, then message will be delivered. If not, then user will get negative delivery report and should re-send message again.
Text message is entered
Phone number
is added
Delivered to recipient (positive delivered report)
Message is sent
Stored on server 12 hours
Start
Type text
Chose phone
number
Click
‘Send’
Yes
No
Delivered until 12 hours
Not delivered to recipient (negative delivered report)
Not delivered until 12 hours
re-send message again

## Slide 8: State Transition
Task: User sends message using mobile phone. He enters a text of a message, and then phone number of recipient and click ‘Send’. Assume that delivery report option is enabled. If user gets positive delivery report, then message will be delivered to recipient. If not, then message will be stored on server for 12 hours. If recipient turns on the phone until 12 hours over, then message will be delivered. If not, then user will get negative delivery report and should re-send message again.
Text message is entered
Phone number
is added
Delivered to recipient (positive delivered report)
Message is sent
Stored on server 12 hours
Start
Type text
Chose phone
number
Click
‘Send’
Yes
No
Delivered until 12 hours
Not delivered to recipient (negative delivered report)
Not delivered until 12 hours
re-send message again
Phone number
is valid
Phone number
is invalid
Check phone number validation

## Slide 9: Thank you
USA TELEPHONE
Toll-Free: 866.687.3588
Office: 239.690.3111
UK TELEPHONE
Tel: 0207.544.8414
GERMAN TELEPHONE
Tel: 0692.602.5857
EMAIL
info@softserveinc.com
WEBSITE:
www.softserveinc.com
EUROPE OFFICES
United Kingdom
Germany
The Netherlands
Ukraine
Bulgaria
US OFFICES
Austin, TX
Fort Myers, FL
Boston, MA
Newport Beach, CA
Salt Lake City, UT